## Slide 1: Assignment 6 Socket Communication
Atul B Prabhakar

## Slide 2: Introduction
Cavli IoT modules (e.g. C17QS) are typically based on Qualcomm chipsets that support AT+QIOPEN and AT+QISEND commands. These allow establishing TCP or UDP socket connections directly from the modem, enabling data communication in IoT scenarios.
What is Socket communication?
Socket communication is a way for two devices (or software processes) to exchange data over a network — such as the internet — using a standard set of protocols like TCP or UDP.

## Slide 3: Objective
Demonstrate how to:
Configure PDP context (data bearer)
Open a TCP connection using AT+QIOPEN
Send data using AT+QISEND
Handle acknowledgments and errors

## Slide 4
1. Prepare PDP Context
AT+CGDCONT=1,"IP","<APN>"
AT+QIACT=1
AT+QIACT?
Defines APN and activates the packet data context
2. Open TCP Connection (AT+QIOPEN)
AT+QIOPEN=1,0,"TCP","192.168.1.100",8000,0,1
Expected sequence:
OK
+QIOPEN: 0,0 ; connectID=0, err=0 (success)

## Slide 5
3. Send Data (AT+QISEND)
AT+QISEND=0,12
> Hello Server<Ctrl+Z>
Indicates connection ID and data length; entering message with <Ctrl+Z>
Response:
SEND OK
4. Close and Deactivate
AT+QICLOSE=0
CLOSE OK

## Slide 6
These commands are supported by:
Cavli C10GS – NB-IoT/2G
Cavli C16QS – LTE Cat 1
Cavli C17QS – LTE Cat 4
Cavli C20QM – LTE Cat 4/6
Cavli CQS290/325 – LTE modules

## Slide 7: Applications
Remote Device Monitoring
Cloud-Connected Sensors
Over-the-Air (OTA) Updates
Vehicle Telematics
Industrial Automation

## Slide 8: Conclusion
Socket communication is a fundamental technology that enables reliable, real-time data exchange between devices over networks using TCP or UDP. In IoT systems like Cavli modules, socket functions are managed using AT commands such as AT+QIOPEN and AT+QISEND, allowing embedded devices to communicate with servers, cloud platforms, or other devices efficiently. Mastering these commands is essential for developing robust and connected IoT applications.